CCBCMD CAMM112 Air Motor Project
March 1, 2015
PES

1. Base
  1. Cut 1/2” x 3” aluminum 6061 stock to 6.25”
  2. Square edges to size and finish using side cutting end mill.
  3. Clamp in vise with parallels to expose 0.31” of edges
  4. Using 1/2” ball mill, machine contours on edges.
  5. Locate holes using prick punch, center punch, and spot drill.
  6. Drill through holes 9/32” and deburr
  7. Using flycutter, finish top surface, removing no more than 0.002”.
  8. Flip over and finish bottom surface.
  9. Countersink holes
  10. Remove from machine and hand file all sharp edges smooth.
2. Manifold
  1. Cut 1” x 1” steel 1018 stock to 4.5”
  2. Mill both ends square and length to 4.255” (0.005” oversize)
  3. Lightly mill stock surfaces square to greater than 0.997” (0.002” oversize)
  4. Layout, locate, drill, and tap two holes in end to match base
  5. Layout and locate one hole on surface “A” and four holes on surface “B”
  6. Drill 3/8” pilot hole in surface “A”
  7. Using 7/16” end mill, make flat bottomed hole 0.50” deep
  8. Tap for 1/4-18 NPT
  9. Countersink to 0.530” D
  10. Drill one hole 0.201” D (#7) 0.62” deep
  11. Tap 1/4-20
  12. Countersink to 0.25” D
  13. Drill two holes 0.156” D, one thru, other 0.5” deep into NPT hole
  14. Drill 0.359” (23/64) thru hole
  15. Ream to 0.375” RC5 fit on 3/8” dowel (-0, +0.0009) for dowel 0.001 to 0.0016 undersize
  16. Countersink to 0.015” over (0.390” D) ?
  17. Chamfer 5 corners 1/16” x 45 degrees (hand file?)
  18. Surface grind all surfaces flat and perpendicular to 63 micro-inch finish.
3. Crankshaft
  1. Cut 0.25” piece of 1.25” diameter round aluminum 6061 stock
  2. Using soft jaws on lathe, face one end flat
  3. Reverse, and face to 0.214” thick
  4. Drill center and follow with 0.359” (23/64) drill
  5. Ream to 0.375” FN2 fit for 3/8” dowel (+0, -0.0006) for dowel 0.001 to 0.0014 oversize
  6. Press dowel into hole
  7. Insert dowel into collet and fasten to rotary table on mill with 1/4” sacrificial spacer
  8. Center mill on dowel and zero DRO or hand dials
  9. Align rotary table to 0 degrees
  10. Move table to 0.050” and drill 0.172” (11/64) hole through piece and into spacer
  11. Ream to 0.1875 FN2 fit for 3/16” dowel (-0, +0.0005) for dowel 0.0007 to 0.001 oversize
  12. Clamp part over hole
  13. Install 1/4” end mill and turn table 180 degrees. Set milling table to 1.125”
  14. Mill down through part into washer
  15. Turn table 90-35 degrees (55 degrees for one section of arc).
  16. Using mill table, mill straight section on one side.
  17. Return to previous position, and turn rotary table 55 degrees in other direction.
  18. Use mill table to complete other side
  19. Use hand file to break sharp edges
  20. Press 3/16” dowel into hole
4. Cylinder
  1. Cut 2.50” piece of 1” x 1” aluminum 6061 square stock.
  2. Lightly mill all surfaces flat and square
  3. Locate center of one end with cross lines using 45 degree or center head on square
  4. Mark location with prick punch and center punch
  5. Secure piece in 4-jaw chuck in lathe, using tailstock center on hole location
  6. Drill a center, followed by a 3/8” diameter drill, to depth of 1.375”
  7. Using a boring bar in the toolholder, adjust carriage stop for depth of 1.350”
  8. Bore hole to 0.625” diameter (use telescoping gauge to check)
  9. Make sure bottom of hole is flat; increase depth and bore deeper if needed
  10. Measure actual depth of hole, and face end until actual depth is 1.344”
  11. Use flycutter to machine surface “A” to 63 micro-inches.
  12. Mark surface “A” with layout dye, and locate positions of two holes 1.250” and 1.750”
  13. Drill one hole 0.156” (5/32) into bore
  14. Drill one hole 0.297” (19/64) thru
  15. Ream 5/16” for shoulder bolt
  16. Use 5/16” locating pin in center of rotary table, and a sacrificial 1/8” to 1/4” spacer
  17. Clamp down to table using 0.625” rod in bore
  18. Use 1/2” radius corner rounding end mill to produce profile per drawing
  19. Spotface 5/16” hole to 0.375” D
  20. Break all sharp edges 0.015 max with hand file
5. Piston
  1. Cut 0.625” steel 1018 round stock to 2.0” long
  2. Face one end
  3. Drill small center hole (optional)
  4. Extend piece so 1.50” extends from chuck
  5. Use small live center to support end in tailstock (optional)
  6. Turn connecting rod to 0.375” diameter 1.25” to square shoulder
  7. Face inside edge of shoulder square.
  8. Reverse piece and hold in chuck using 0.375” connecting rod (maybe use a collet)
  9. Face end of piston to 0.531” long
  10. Mark 1.750” on end of connecting rod
  11. Hold piston in chuck and face end of connecting rod to 1.750”
  12. Mark 0.188” from end of connecting rod
  13. Use file to chamfer edges 0.005-0.010”
  14. Support connecting rod on parallels in milling vise
  15. Locate center of shaft and end of shaft with edge finder, and set DRO or dials
  16. Use spotting drill or center drill to locate hole
  17. Drill 0.172” (11/64) diameter hole
  18. Ream to RC7 fit for 3/16” dowel (0.1875 to 0.1887 for 0.1856 to 0.1863 dowel)
6. Flywheel
  1. Cut 2.00” diameter aluminum 6061 rod to 1.25” long
  2. Face both ends square
  3. Drill center and support with live center in tailstock
  4. Turn to shoulder 0.875” diameter 0.380 to 0.390” long
  5. Face shoulder smooth and square
  6. Remove live center and replace with drill chuck.
  7. Drill 0.359” (23/64) hole through flywheel
  8. Bore 3/8” for RC6 fit on dowel (0.375”-0.3765” for 0.3731” to 0.374” shaft)
  9. Face shaft connector to 0.375” long
  10. Reverse part in chuck and face outside end to 1.125” total length
  11. Chamfer all edges with file, and polish surfaces with abrasive cloth
  12. Support flywheel in milling vise using V-block
  13. Locate center and edge using edge finder, and set DRO or dials
  14. Locate 0.188” from end and use spotting drill or center drill to start hole
  15. Drill 0.201” (#7) into bore
  16. Tap hole to 1/4-20
  17. Countersink to 1/4” diameter