Technology of EVs
The concept, design, and manufacture of Electric Vehicles (EVs) involves many aspects of technology, particularly physics, chemistry, electronics, mechanical engineering, and software programming.
I will begin with the physical concepts that are involved with all vehicles.

---
EV Calculator
- Force and weight (pounds, kilograms)
- Velocity or speed (MPH, RPM)
- Acceleration (gravity, change of velocity)
- Power (watts, horsepower)
- Energy and work (joules, watt-hours)
- Voltage and current
- Efficiency
- Aerodynamic drag and rolling friction

---
1000 kg, 62 MPH, 10% slope

---
1000 kg, 4% slope, 30 MPH

---
Electric Motors
- Brushed DC PM
- High Torque
- High cost/maintenance
- Simple control (PWM)
- AC Induction Motor
- Moderate torque
- Low cost/maintenance
- Complex control (VFDs)

---
Energy storage
- Liquid fuels
- Gasoline
- Diesel
- Batteries
- Lead-acid
- Lithium
- New technologies

---
Chargers
In-vehicle DIY 12 kW battery charger
- EVSE
- CHEdeMO

---
EV Concerns
- Battery fires
- Dreamliner lithium battery
- Li-Ion vs LiFePO4
- Battery Management Systems
- Accidents
- Tesla battery fire
- Compare to gas-fueled fire
- Safety measures

---
DIY Electric Cars
- Forkenswift
- Recycled/reused parts
- Less than $1000
- Limited range/speed
- Panic In Detroit
- 1000 kW (1300 HP)
- 0-60 in 1 sec
- 200 MPH top speed

---
Other DIY EVs
- Woody's Tractor
- 16 kW (20 HP)
- 48 VDC LiFePO4
- Ripperton Super Bike
- 115 kW (140 HP)
- 127 MPH